## Slide 1: Binary Subtraction
Introduction to Data Concepts
By Tina Blumenthal

## Slide 2
Binary subtraction is simple (well in theory)
There is a rule that we will eventually learn.
We aren’t interested in how the computer physically does it.
Binary Subtraction

## Slide 3
Computers achieve subtraction by adding the negative value, storing the negative number in a form called Two’s Complement.
Now that sure sounds confusing!!!
So we’ll look at what we mean by Two’s complement and then we’ll look at an example
Subtracting in Binary

## Slide 4
Remember the computer “thinks/works” in binary
  To us it is easy to do subtraction in base 10
  We are trying to appreciate how computers do subtraction
The Two’s Complement method does subtraction by using addition.
  If a computer has the components to do addition it can do subtraction
Two’s Complement

## Slide 5
9 – 3 = 6
  Note 10 – 3 = 7
  9 + 7 = 16 (9 – 3 = 6)
  Drop the 1
6 – 2 = 4
  Note 10 – 2 = 8
  6 + 8 = 14 (6 – 2 = 4)
  Drop the 1
Background

## Slide 6
18 – 11 = 7
  Note 20 – 11 =9
  18 + 9 = 27 (18 – 11 = 7)
  Drop the 2
96 – 60 = 36
  Note 100 – 60 = 40
  96 + 40 = 136 (96 – 60 =36)
  Drop the 1 (Left most number)
Background

## Slide 7
3 – 9 = -6
  Note 10 – 9 = 1
  3 + 1 = 4
  10 – 4 = 6 (3 – 9 = -6)
  Take the complement again
Background

## Slide 8
80 – 93 = -13
  Note 100 – 93 = 7
  80 + 7 = 87
  100 – 87 = 13 (80 – 93 = -13)
  Take the complement again
This is the rule we use in subtraction
Background

## Slide 9
Two’s complement is used by computers to store negative numbers.
For binary numbers it relies on using the most significant bit to indicate the sign of the number.
This is the leftmost bit, a 0 indicates a positive number and a 1 indicates a negative number.
Using 8 bits, the leftmost bit is the sign leaving 7 bits for the number.
Two’s Complement

## Slide 10
Using 8 bit, 00100111 represents positive 39
  The left most zero indicates positive
  100111 is the same as 39
  32 + 4 + 2 + 1 = +39
32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 1 | 1
Two’s Complement

## Slide 11
To represent a negative number we start with the positive number, we flip all the bits and then add 1
  To represent – 29
  calculate 29 as an 8 bit value
  00011101
  Flip the bits
  11100010
  Add 1
  11100011
Two’s Complement

## Slide 12
So if we have a number where the leftmost bit is 1, we know it is negative.
To determine the decimal equivalent we
  Step 1: flip the bits
  Step 2: add 1
  Step 3: convert to decimal and make the result negative
Two’s Complement

## Slide 13
So what number is represented by 11100011?
Left most bit is 1 so it’s negative
Flip all the bits
  00011100
Add 1
  00011100 + 1 = 00011101
Converts to - 29
Two’s Complement

## Slide 14
Subtracting Binary
using
Two’s Complement

## Slide 15
 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
 |  |  |  | +1
1 | 1 | 0 | 0 | 0
 | 1 | 1 | 0 | 0
(1)0 | 0 | 1 | 0 | 0
Which is (4)10 ignore the left most number
12 - 8

## Slide 16
 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
 |  |  |  | +1
1 | 0 | 1 | 1 | 1
 | 1 | 1 | 1 | 0
(1)0 | 0 | 1 | 0 | 1
14 - 9
Which is (5)10 ignore the left most number

## Slide 17
Write the second number (B)
Change the
  0 to 1
  1 to 0
Add +1
Add this new number to the first (A)
Ignore the carry
Rules for A - B

## Slide 18
1 | 0 | 0 | 1
0 | 1 | 1 | 0
 |  |  | +1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
(1)0 | 0 | 1 | 0
1011 - 1001

## Slide 19
1 | 0 | 1 | 1
0 | 1 | 0 | 0
 |  |  | +1
0 | 1 | 0 | 1
1 | 1 | 0 | 1
(1)0 | 0 | 1 | 0
1101 - 1011

## Slide 20
1 | 1 | 0 | 0
0 | 0 | 1 | 1
 |  |  | +1
0 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
0 | 0 | 0 | 0
 |  |  | 1
 |  |  | -1
1011 - 1100
When the second number is greater than the first do 2’s complement again

## Slide 21
1 | 1 | 0 | 1
0 | 0 | 1 | 0
 |  |  | +1
0 | 0 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
 |  |  | 1
 | -1 | 0 | 0
1001 - 1101
When the second number is greater than the first do 2’s complement again

## Slide 22
Change binary number on second line (0 to 1 )
Add 1
Add result to top line
(Temporary Answer)
Is 2nd number > 1st number (top 2 lines)
No then STOP there
  Temporary Answer is the Answer
Yes
  Change second line (0 to 1 )
  Add 1
  Result of this is the answer
  Include negative sign
Summary

## Slide 23
11100 – 10011 =
101101 – 100011 =
110001 – 101011 =
110010 - 11101 =
100100 – 11000 =
1010110 - 11011 =
Try these problems

## Slide 24
11100 – 10011 = 1001
101101 – 100011 = 1010
110001 – 101011 = 110
110010 - 11101 = 10101
100100 – 11000 = 1100
1010110 - 11011 = 111011
Do you agree with these answers?
Answers

## Slide 25
100011 - 101000 =
101010 - 110001 =
100111 - 101011 =
110000 – 110100 =
Try these problems

## Slide 26
100011 - 101000 = -101
101010 - 110001 = -111
100111 - 101011 = -100
110000 – 110100 = -100
Do you agree with these answers?
Answers